## Slide 1
DDCA PROJECT
Design and Simulation of Digital Access Card Verification Using XOR/NOR Logic
Subject: DDCA – Digital Design and Computer Architecture
Guide: Dr. Venkanna Isampalli
TEAM MEMBERS
2620040061
Pranathi Kusi
2620030115
K. Rishika
2620030083
Y. Naga Amrutha
2620030098
P. Renu Sree
Koneru Lakshmaiah Education Foundation
Department of Freshman Engineering | Academic Year 2026–27
ACCESS CARD
CARD ID
1 0 1 0
S
E
XOR
NOR
ACCESS GRANTED
Bitwise XOR comparison → NOR match detection
Notes: Title slide. Replace the LOGO box with the university logo.

## Slide 2: What Is Digital Access Card Verification?
PROJECT INTRODUCTION
What it is
A digital circuit reads the ID on a card and checks whether it matches the ID stored in the system before allowing entry.
Why it is useful
It automates entry control for labs, offices and libraries with a fast, rule-based yes/no decision and no manual checking.
How the comparison works
A stored 4-bit ID (S3–S0) is compared bit by bit with an entered 4-bit ID (E3–E0).
XOR gates
Compare each bit pair; output 1 on a mismatch
NOR logic
Outputs 1 only when no bit mismatches
Output
ACCESS GRANTED or ACCESS DENIED
SYSTEM OVERVIEW
Stored ID
S3 S2 S1 S0
Entered ID (card)
E3 E2 E1 E0
4 × XOR bit comparators → X3 X2 X1 X0
NOR match detector → MATCH
ACCESS GRANTED
MATCH = 1
ACCESS DENIED
MATCH = 0

## Slide 3: Abstract, Problem Statement and Objectives
PROJECT OVERVIEW
Abstract
This project designs and simulates a four-bit digital access card verification circuit. Four XOR gates compare a stored ID with an entered ID bit by bit, and NOR-based logic asserts MATCH only when every bit agrees. MATCH drives the ACCESS GRANTED and ACCESS DENIED indicators. The design is verified with truth tables and simulated in Logisim Evolution.
Problem Statement
Access control needs an instant, reliable decision on whether a presented ID is authorised; manual checking is slow and error-prone. The task is to design a simple combinational circuit that compares two 4-bit binary IDs and outputs a clear grant or deny decision.
Objectives
1
Design a four-bit digital access verification system.
2
Compare entered and stored binary IDs.
3
Detect mismatches using XOR gates.
4
Detect a complete match using NOR logic.
5
Generate access-granted and access-denied outputs.
6
Verify the design using truth tables and Logisim simulation.

## Slide 4: Course Outcomes (COs)
COURSE MAPPING
CO | Course outcome (summary) | How this project connects | Status
CO1 | Represent digital information with binary number systems and logic gates | IDs are 4-bit binary numbers; XOR and NOR gates make the decision | Applied
CO2 | Design and simulate combinational logic and a simple ALU | The verifier is a combinational circuit; its NOR stage works like an ALU zero flag | Applied
CO3 | Design sequential logic: flip-flops, registers, counters and FSMs | Add an attempt counter and a lockout state machine | Extension
CO4 | Design the register file and memory subsystem of a processor | Store many authorised IDs in a register file or memory | Extension
CO5 | Analyse RISC-V instructions and the single-cycle processor | The same check in software: xor, then beqz on the result | Extension
CO6 | Extend a processor with architectural features and peripherals | Interface an RFID reader and door lock as peripherals | Extension
Applied: covered directly by this project. Extension: reached through the project's future scope.

## Slide 5: Components Required and Scope
SYSTEM REQUIREMENTS
Component | Qty | Purpose
Stored-ID input bits (S3–S0) | 4 | Hold the authorised card ID
Entered-ID input bits (E3–E0) | 4 | Represent the ID read from the card
2-input XOR gates | 4 | Compare each bit pair; output 1 on a mismatch
NOR-based match detector | 1 | MATCH = 1 only when all XOR outputs are 0
Output indicators (LEDs) | 2 | GRANTED = MATCH; DENIED = NOT MATCH (one inverter)
Logisim Evolution | — | Build, simulate and verify the circuit
The NOR detector can be one 4-input NOR gate or an equivalent network of 2-input NOR gates (slide 8).
PROJECT SCOPE
Complete gate-level design
Covers the full path from bit comparison to the final GRANTED / DENIED decision.
Verified in Logisim Evolution
Every test case can be built, run and checked against the truth table in simulation.
Configurable ID inputs
Eight input pins represent the stored and entered card IDs and can be set to any value.
Future scope: build the verified design as a hardware prototype with logic ICs and a card reader.

## Slide 6: System Block Diagram
ARCHITECTURE
STORED ID
S3
S2
S1
S0
From system memory
ENTERED ID
E3
E2
E1
E0
From access card
4 × BITWISE XOR COMPARATORS
S3–S0
E3–E0
X3 = S3 ⊕ E3
X3
X2 = S2 ⊕ E2
X2
X1 = S1 ⊕ E1
X1
X0 = S0 ⊕ E0
X0
MISMATCH SIGNALS
NOR-BASED MATCH DETECTION
NOR
MATCH = NOT(X3 + X2 + X1 + X0)
MATCH
ACCESS GRANTED
when MATCH = 1
ACCESS DENIED
when MATCH = 0
Stored + Entered ID → Bitwise XOR comparators → Mismatch signals X3–X0 → NOR match detection → Access Granted / Denied

## Slide 7: XOR Gate Operation: Bitwise Comparison
LOGIC STAGE 1
Rule: XOR outputs 0 when its inputs are equal and 1 when they differ, so each XOR output flags one mismatched bit.
A
B
XOR
Y = A ⊕ B
A | B | Output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Equal inputs → 0 (green) Different → 1 (red)
BIT-LEVEL EQUATIONS
X3 = S3 XOR E3
X2 = S2 XOR E2
X1 = S1 XOR E1
X0 = S0 XOR E0
Matching example: 1010 vs 1010
Stored S
1
0
1
0
Entered E
1
0
1
0
XOR X
0
0
0
0
All bits equal → XOR = 0000 → no mismatch
Mismatching example: 1010 vs 1000
Stored S
1
0
1
0
Entered E
1
0
0
0
XOR X
0
0
1
0
Bit 1 differs → XOR = 0010 → mismatch on X1

## Slide 8: NOR Logic: Detecting a Complete Match
LOGIC STAGE 2
Rule: a NOR output is 1 only when all of its inputs are 0. So MATCH = 1 only if X3–X0 are all 0.
MATCH = NOT(X3 OR X2 OR X1 OR X0)
ACCESS_GRANTED = MATCH
ACCESS_DENIED = NOT MATCH
A | B | A NOR B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
2-input NOR truth table. A 4-input NOR is 1 for only one of 16 input patterns: 0000.
4-INPUT NOR MATCH DETECTOR
X3
X2
X1
X0
NOR
MATCH
GRANTED
DENIED
EQUIVALENT NETWORK USING ONLY 2-INPUT NOR GATES
X3
X2
X1
X0
N1
N2
N3
N4
MATCH
N1 = NOR(X3, X2)
N3 = NOR(N1, N1) = X3 + X2
N4 = NOR(N2, N2) = X1 + X0
MATCH = NOR(N3, N4)

## Slide 9: Boolean Expression and Logic Simplification
BOOLEAN ANALYSIS
COMPLETE EXPRESSION
MATCH = NOT[(S3 XOR E3) OR (S2 XOR E2) OR (S1 XOR E1) OR (S0 XOR E0)]
EQUIVALENT EXPRESSION
MATCH = (S3 XNOR E3) AND (S2 XNOR E2) AND (S1 XNOR E1) AND (S0 XNOR E0)
Why they are equal: De Morgan's law gives NOT(A + B + C + D) = A'·B'·C'·D', and NOT(Si XOR Ei) = Si XNOR Ei.
Purpose of simplification and K-maps
Simplification cuts gate count, wiring and delay without changing the output.
A Karnaugh map groups adjacent 1s to find the minimal sum-of-products form.
The full comparator has 8 inputs (256 rows), so one 4-variable K-map cannot represent it.
The K-maps here cover two valid sub-functions of the design.
K-map: MATCH(X3, X2, X1, X0)
X3X2 \ X1X0 | 00 | 01 | 11 | 10
00 | 1 | 0 | 0 | 0
01 | 0 | 0 | 0 | 0
11 | 0 | 0 | 0 | 0
10 | 0 | 0 | 0 | 0
Single 1 at 0000 → MATCH = X3'·X2'·X1'·X0' (a 4-input NOR).
K-map: bit-slice Mi(Si, Ei)
Si \ Ei | 0 | 1
0 | 1 | 0
1 | 0 | 1
Diagonal 1s cannot be grouped → Mi = Si'Ei' + SiEi = Si XNOR Ei.

## Slide 10: Truth Table and Test Cases
VERIFICATION
Stored ID | Entered ID | XOR Outputs | Match | Decision
0000 | 0000 | 0000 | 1 | GRANTED
1010 | 1010 | 0000 | 1 | GRANTED
1111 | 1111 | 0000 | 1 | GRANTED
1010 | 1000 | 0010 | 0 | DENIED
1010 | 0010 | 1000 | 0 | DENIED
1100 | 1101 | 0001 | 0 | DENIED
0101 | 1010 | 1111 | 0 | DENIED
Bit order is b3 b2 b1 b0 (MSB → LSB). XOR outputs are listed as X3 X2 X1 X0.
Access granted
All XOR outputs are 0000 → the NOR output is 1 → MATCH = 1 → access is granted.
Access denied
Any XOR output is 1 (a mismatch) → the NOR output is 0 → MATCH = 0 → access is denied.

## Slide 11: Logisim Circuit Diagram
CIRCUIT IMPLEMENTATION
GATE-LEVEL CIRCUIT
S3
E3
XOR
X3
S2
E2
XOR
X2
S1
E1
XOR
X1
S0
E0
XOR
X0
NOR
MATCH
ACCESS
GRANTED
ACCESS
DENIED
Notes: Paste your Logisim Evolution screenshot over the dashed box on the right, then delete the box and its text.

## Slide 12: Simulation Procedure and Results
SIMULATION
Build and test in Logisim Evolution
1
Place the eight input pins: S3–S0 and E3–E0.
2
Add four 2-input XOR gates.
3
Connect each stored bit and its matching entered bit (Si, Ei) to the same XOR gate.
4
Connect XOR outputs X3–X0 to the NOR-based detector.
5
Add output LEDs: GRANTED from MATCH, DENIED through a NOT gate.
6
Toggle the pins with the Poke tool to test matching and mismatching IDs.
7
Compare every output with the truth table.
EXPECTED RESULTS
Derived from the Boolean design, not from a simulation run. Fill in the Observed column after simulating.
Test case | S / E | X3–X0 | MATCH | Expected | Observed
Identical IDs | 1010 / 1010 | 0000 | 1 | GRANTED | 
One-bit mismatch | 1010 / 1000 | 0010 | 0 | DENIED | 
Two-bit mismatch | 1100 / 1111 | 0011 | 0 | DENIED | 
All bits differ | 0101 / 1010 | 1111 | 0 | DENIED | 
Pass criterion: the GRANTED LED lights only when all four XOR outputs are 0; the DENIED LED lights for every other input combination.

## Slide 13: Advantages
EVALUATION
Simple digital logic design
Just XOR, NOR and NOT gates; easy to read, build and explain.
Fast comparison
Only two gate levels between the inputs and the decision.
Easy to simulate
Builds in Logisim in minutes; every case checks against the truth table.
Modular implementation
Each extra ID bit adds one XOR gate and one NOR input.
No programming required
Pure hardware logic; the decision needs no software.
Low hardware cost
Can be built from three common 74-series logic ICs.

## Slide 14: Limitations
EVALUATION
Each limitation of the prototype has a clear upgrade path.
CURRENT LIMITATION
PLANNED IMPROVEMENT
1
Only four-bit IDs
Extend the ID width to 8, 16 or 32 bits
2
No physical card reader
Integrate an RFID or NFC reader
3
No database or user management
Store authorised IDs in memory or a register file
4
Only 16 possible ID combinations
Wider IDs give 2ⁿ combinations (65,536 at 16 bits)
5
Not secure enough for real-world access control
Add attempt counting, lockout and stronger authentication

## Slide 15: Applications and Future Scope
OUTLOOK
Applications
Educational demonstrations
Teaching comparators, XOR and NOR logic in DDCA labs.
Laboratory access prototypes
Concept model for controlled lab entry.
Library and office access
Basis for card-based entry in shared spaces.
Future Scope
1
Extend the ID width
2
Add an attempt counter and lockout logic
3
Integrate an RFID or NFC reader
4
Add a microcontroller and display
5
Introduce stronger authentication safeguards

## Slide 16: Conclusion
SUMMARY
Four XOR gates compare the stored and entered IDs bit by bit, producing a mismatch vector that is 0000 only when the IDs are identical. NOR-based logic turns this vector into a single MATCH signal that drives the ACCESS GRANTED and ACCESS DENIED outputs.
XOR compares
Each XOR flags one mismatched bit, giving X3–X0.
NOR decides
MATCH = 1 only when no bit mismatches, so access is granted only for the correct ID.
Simulation verifies
Truth tables and Logisim confirm the design, demonstrating combinational logic design and digital verification.

## Slide 17: GitHub Repository
PROJECT FILES
https://github.com/renusree88/KLHB--Design-and-Simulation-of-Digital-Access-Card-Verification-Using-XOR-NOR-thttps://github.com/renusree88/KLHB--Design-and-Simulation-of-Digital-Access-Card-Verification-Using-XOR-NOR-Logic.git https://github.com/renusree88/KLHB--
REPOSITORY
Repository contents
Circuit diagram
Gate-level diagram of the verifier
Simulation file
Logisim Evolution .circ file
Report
Full project report
PPT and poster
Presentation slides and project poster
README: project description, components, working and setup steps. All team members' contributions are documented.
Notes: Replace the repository link with your team's actual GitHub URL.

## Slide 18
THANK YOU
Questions and Discussion
Pranathi Kusi · K. Rishika · Y. Naga Amrutha · P. Renu Sree