## Slide 1
NOR LOGIC
Design and Simulation of a Fundamental Digital Logic Gate
Digital Logic • Boolean Algebra • Circuit Simulation
PROJECT PRESENTATION
10-slide overview
01 / 10
PROJECT TEAM
2620040061 – Pranathi Kusi
2620030115 – K. Rishika
2620030083 – Y. Naga Amrutha
2620030098 – P. Renu Sree

## Slide 2
1. What Is Digital Logic?
The foundation of how computers make decisions
02 / 10
A computer accepts input, processes information, stores data, and produces output.
Digital circuits represent information using two stable states: 0 and 1.
Logic gates process binary inputs and produce binary outputs.
Small gates combine into larger systems such as adders, memory, and CPUs.
INPUT
Switches, buttons, or sensor signals
PROCESS
Logic gates apply Boolean rules
OUTPUT
LED, display, or control signal

## Slide 3
2. Understanding the NOR Gate
NOR means NOT-OR: the output is 1 only when every input is 0
03 / 10
First, OR gives 1 when at least one input is 1.
NOR reverses the OR output using NOT.
Boolean expression: Y = ¬(A + B)
NOR is a universal gate: any Boolean circuit can be built using only NOR gates.
NOR
A
B
Y = ¬(A + B)
Y is HIGH only for A = 0 and B = 0

## Slide 4
3. NOR Gate Truth Table
Check all possible combinations of two binary inputs
04 / 10
Input A
Input B
Output Y
0
0
1
0
1
0
1
0
0
1
1
0
Key observation
Only the 00 input combination produces an output of 1. Every other combination produces 0.
This table is the specification used to test the simulated circuit.

## Slide 5
4. Boolean Expression & Logic Symbols
Translate the required behaviour into a simple expression
05 / 10
OR OPERATION
A + B = 1 if A or B (or both) is 1
NOT OPERATION
¬X flips a bit: 0 becomes 1; 1 becomes 0
NOR OPERATION
Y = ¬(A + B)
Example
If A = 0 and B = 1: A + B = 1, so Y = ¬1 = 0.
The plus sign means OR in Boolean algebra—not ordinary arithmetic addition.

## Slide 6
5. Why Is NOR Called a Universal Gate?
Build other basic gates from NOR gates alone
06 / 10
NOT
A NOR A = ¬A
OR
(A NOR B) NOR (A NOR B) = A + B
AND
(A NOR A) NOR (B NOR B) = A · B
WHY IT MATTERS
A single gate type can implement many logic functions, simplifying circuit design and helping explain how complex hardware is built from simple building blocks.

## Slide 7
6. Simulating a NOR Circuit
A simple workflow in Logisim Evolution or Digital
07 / 10
1
Place a NOR gate
Choose a 2-input NOR gate from the gate library.
2
Add inputs
Connect two switches or input pins to A and B.
3
Connect output
Attach an LED or output pin to Y.
4
Test combinations
Try 00, 01, 10, and 11 and compare with the truth table.
Good practice: save the circuit file and record the test results.

## Slide 8
7. Where NOR Fits in a Computer
Logic gates combine to create larger digital systems
08 / 10
GATE LEVEL
NOR, AND, OR, XOR, NOT
CIRCUITS
Adders, multiplexers, decoders
CPU BLOCKS
ALU, control, registers
COMPUTER
Runs instructions
A NOR gate does not make a full CPU by itself—but it demonstrates how complex behaviour can emerge from simple, predictable rules.
The same design mindset is used when building an ALU and studying a RISC-V processor.

## Slide 9
8. Testing, Results & Applications
Verify the circuit against the specification
09 / 10
Expected result: output is 1 only when both inputs are 0.
Test cases: 00 → 1, 01 → 0, 10 → 0, 11 → 0.
If every simulated output matches the truth table, the NOR circuit is functioning correctly.
Applications: control logic, simple decision circuits, digital design learning, and universal-gate implementations.
EXPECTED
Y = ¬(A + B)
VERIFICATION
Compare simulation with all 4 truth-table rows
CONCLUSION
Simple rule. Reliable result.

## Slide 10
THANK YOU
Questions?
NOR Logic • Digital Systems • Circuit Simulation
10 / 10